## Slide 1
William Stallings Computer Organization and Architecture
6th Edition
Chapter 9
Computer Arithmetic

## Slide 2
2.1 Introduction to Arithmetic and Logical unit, Computer Arithmetic: Fixed and Floating point numbers, Signed numbers, Integer Arithmetic, 2’s Complement arithmetic
2.2 Booth’s Recoding and Booth’s algorithm for signed multiplication, Restoring division and non-restoring division algorithms
2.3 IEEE floating point number representation and operations: Addition. Subtraction, Multiplication and Division. IEEE standards for Floating point representations :Single Precision and Double precision Format

## Slide 3
Arithmetic & Logic Unit
Does the calculations
Everything else in the computer is there to service this unit
Handles integers
May handle floating point (real) numbers
May be separate FPU-floating-point unit (FPU), which operates on floating point numbers. (maths co-processor)

## Slide 4: ALU Inputs and Outputs

## Slide 5
Operands for arithmetic and logic operations are presented to the ALU in registers, and the results of an operation are stored in registers.
These registers are temporary storage locations within the processor that are connected by signal paths to the ALU.
The ALU may also set flags as the result of an operation.
The flag values are also stored in registers within the processor.
The processor provides signals that control the operation of the ALU and the movement of the data into and out of the ALU.

## Slide 6: Addition and Subtraction
Normal binary addition
Monitor sign bit for overflow
Take twos compliment of substahend and add to minuend
— i.e. a - b = a + (-b)
So we only need addition and complement circuits
A | B | Sum
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0, Carry 1
1 | 1 | 1,Carry 1

## Slide 7: Example of 2’s Compliment

## Slide 8
Find 2’s compliment
1000
0100
111001
101010
100000

## Slide 9: Hardware for Addition and Subtraction

## Slide 10: Booth’s Algorithm

## Slide 11
M =7
Q =3
M = 0 1 1 1
Q = 0 0 1 1
- M = 1 0 0 1
Q0 | Q-1 | Result
0 | 0 | Only shift
1 | 1 | 
0 | 1 | A=A + M ,then shift
1 | 0 | A= A – M , then shift

## Slide 12: Example of Booth’s Algorithm:7(M)*3(Q)
Answer is in A and Q0001 0101 =21

## Slide 14
Examples-size of n determines answer
Solve using Booths Algorithm A. M = 5 , Q = 5
B. M = 12, Q = 11
C. M = 9, Q = - 3
D. M = -13 ( 0011 ) , Q = 6
-M=13 (1101)
A. M = -19 , Q = -20

## Slide 15
Division
More complex than multiplication
Negative numbers are really bad!
Based on long division

## Slide 16: Division of Unsigned Binary Integers
001111
1011
100
00001101 1011 10010011
1011
001110
1011
Quotient
Dividend
Remainder
Partial Remainders
Divisor

## Slide 17: Flowchart for Restoring Division

## Slide 25: Solve using Restoring Division
A. M = 5 , |  | Q = 5 , A=0000 , Q=0010
B. M = 12, |  | Q = 26, A=00010 , Q= 00010
C. M = 9, |  | Q = 19 , A=00001 , Q =00010
D. M = 32 | , | Q = 59, A=011011, Q=000001
E. M = 17 | , | Q = 42, A=001000 , Q=000010

## Slide 29: Solve using Non Restoring
A. M = 5 , |  | Q = 5,A=0000,Q=0001.
B. M = 12, |  | Q = 26,A=000010, Q=000010.
C. M = 9, |  | Q = 19,A=00001,Q=00010.
D. M = 32 | , | Q = 59,A=011011,Q=000001.
E. M = 17 | , | Q = 42,A=001000,Q=000010

## Slide 30: Booths Recoding / Bit pair recording
STEPS

## Slide 35
Solve using Booths Recoding
1. M= 5 , Q = 4 (4 bits)= 00010100 (20)
2. M=9 , Q = -6 (5 bits)=11110 01010 (-54)
3. M=15 , Q=-10 (5 bits)=11011 01010(-150)
4. M= -13 ,Q = -20 (6 bits )=000100000100(260)

## Slide 36
Sample mix problems-Kindly refrain referring to flowchart.
1. Booth’s Algorithm = 000 100 000 100(260)
A= 110011 (Multiplicand ) B= 101100 (Multiplier)
2. Booth’s Recoding = 0110 1010/11011 01010
M= ( 15 ) Q= ( -10 )
Non Restoring Division
M=11 , Q= 21 , A= 01010 , Q= 00001
Restoring Division
M=14 , Q= 15, A=00001 , Q = 00001

## Slide 37: Floating Point
• A floating point number, is a positive or negative whole number with a decimal point. For example, 5.5, 0.25, and -103.342 are all floating point numbers, while 91, and 0 are not
+/- .significand x 2exponent
Misnomer
Point is actually fixed between sign bit and body of mantissa
Exponent indicates place value (point position)
Sign bit | Biased Exponent | Significand or Mantissa

## Slide 39: Floating Point Examples
Typical 32-Bit Floating-Point Format
The leftmost bit stores the sign of the number
The exponent value is stored in the next 8 bits.
The representation used is known as a biased representation.
A fixed value, called the bias, is subtracted from the field to get the true exponent value.

## Slide 40: Signs for Floating Point
Mantissa is stored in 2s compliment
Exponent is in excess or biased notation
—e.g. Excess (bias) 128 means
—8 bit exponent field
—Pure value range 0-255
—Subtract 128 to get correct value
—Range -128 to +127

## Slide 41: Expressible Numbers

## Slide 42
IEEE 754
Standard for floating point storage
developed to facilitate the portability of programs from one processor to another
Defines 32 and 64 bit standards with 8 and 11 bit exponent respectively
the standard defines two extended formats, single and double, whose exact format is implementation dependent.
The extended formats include additional bits in the exponent (extended range) and in the significand (extended precision).
The extended formats are to be used for intermediate calculations.
Extended formats (both mantissa and exponent) for intermediate results

## Slide 43: IEEE 754 Formats
32 BIT
64 BIT
(1.N)2E-127
(1.N)2E-1023

## Slide 44: Steps
1. Convert Decimal to Binary
2. Normalization
— Rewriting Step 1 into (1.N) form
— Ex: 1 1 1 . 0 1 1 = 1 . 1 1 0 1 1 X 2 2
Exponent
— Ex: 0 . 0 0 0 1 0 = 0 0 0 0 1 . 0 X 2 -4
3.Biasing
— Applying Single Precision (E – 1 2 7) & Double Precision ( E – 1 0 2 3 ) on exponent from Step 2
4. Representation in Single (32 bit )and Double Precision (64 bit ) Format

## Slide 46: Solved Example

## Slide 50: Solve
25.44
SP- 0|100000|1001 0111 0000 1010 0011 110
DP- 0|10000000011|1001 0111 0000 1010 0011 110
0.00635
SP- 0|1110111|00000001101000…
DP- 0|1111110111|00000001101000… SP- 1 | 10000101| 1111 010001
DP- 1 | 10000000101| 1111 010001
-125.10
-13.54
SP- 1|10000010|10110001010
DP- 1|10000000010|10110001010

## Slide 51: Sample Problems to Solve
1) 178.1875
SP 0|10000110|01100100011 DP 0|10000000110|
1) 309.175
SP 0|10000111|01011101001011 DP 0|10000000111|
1) 1259.125
SP 0|10001001|0011101011001000…(9 zeroes) DP 0|10000001001|010100111100
1) 0.0625
SP 0|01111011|0000000…. DP 0|01111111|00000…..

## Slide 52: Division of signed numbers

## Slide 55
Solve
a) 7 / -3
b) -7 (Q) / 3 (M)
c) -7 (Q) / -3 (M)

## Slide 59
Dividend negative  Remainder –ve

## Slide 61
4 phases of FP Arithmetic +/-
Check for zeros
Align significands (adjusting exponents)
Add or subtract significands
Normalize result

## Slide 62
Floating Point Addition
Add the following two decimal numbers in scientific notation:
8.70 × 10-1 with 9.95 × 101
Rewrite the smaller number such that its exponent matches with the exponent of the larger number.
8.70 × 10-1 = 0.087 (Note ! ) × 101

## Slide 63
Add the mantissas
9.95 + 0.087 = 10.037 and
write the sum 10.037 × 101
Put the result in Normalised Form 10.037 × 101 = 1.0037 × 102
(shift mantissa, adjust exponent)

## Slide 64: Check for overflow/underflow of the exponent after normalisation
Overflow
The exponent is too large to be represented in the Exponent field
Underflow
The number is too small to be represented in the Exponent field

## Slide 65
Round the result
If the mantissa does not fit in the space reserved for it, it has to be rounded off.
For Example: If only 4 digits are allowed for
mantissa
1.0037 × 102 ===> 1.004 × 102

## Slide 66
FP Addition & Subtraction Flowchart

## Slide 67
FP Arithmetic x/
Check for zero
Add/subtract exponents
Multiply/divide significands (watch sign)
Normalize
Round
All intermediate results should be in double length storage

## Slide 68: Floating Point Multiplication

## Slide 69: Floating Point Division